flame m0dul kit / Acrylic glass m0dul for the r0ket / kiu/muccc / Rev B	10 EUR
Remarks / The kit contains more capacitors/resistors than needed (spare parts) / The packaging of the capacitor/resistors are color coded / Do NOT solder the LED before attaching the acrylic glass / Assembly / BOTTOM: Solder resistor R1/100k (RED). / BOTTOM: Solder resistor R2/60|65 (GREEN). / TOP: Solder IC U1/PCA9553. Be aware of the orientation! The slightly beveled side must be left (yellow line). The imprint “NXP” must not be upside down. / TOP: Solder capacitor C1/100nF (BLUE). / BOTTOM: Attach acrylic glass. Etched side facing away from the m0dul. Fixate with screws. Heads on TOP - nuts on BOTTOM. / BOTTOM: Solder U2/LED. Align LED with edge of acrylic glass. / BOTTOM: Solder stack through connectors. Insert from TOP. Female sockets are on TOP - male pins on BOTTOM. Optional: Shorten pins by 5mm. / Run / Turn r0ket off / Plug flame m0dul onto r0ket / Turn r0ket on / Shout out loud: "Booster ignition and liftoff!" / Help / Dig through the r0ket wiki, join the IRC channel or find someone from team r0ket at Fpletzvillage. / Links / https://github.com/kiu/flame / https://r0ket.badge.events.ccc.de / https://events.ccc.de/camp/2011/wiki/Fpletzvillage

TOP / C1 100nF (BLUE) / U1 PCA9533
BOTTOM / R1 100k (RED) / R2 60|65 (GREEN) / U2 LED